## Slide 1: Next-Generation Smart Integrated City Infrastructure With IoT Automation,Multi-VLAN Segmentation and Advanced Cybersecurity Enforcement. Prepared for: Practicum Defense Committee, Department of Computer Science and Engineering
Supervised By: Prepared By:
Mahedi Hasan Nabidur Rahaman
Lecturer ID: 22103011
Department of Computer Science and Engineering, IUBAT.
Date:Sunday, 25 January,2026
IUBAT-International University of Business Agriculture and Technology

## Slide 2: Contents
Organizational Overview
Introduction
Existing Network of Digi Jadoo Broadband Limited(Mohammadi Group)
Proposed Network for Digi Jadoo Broadband Limited(Mohammadi Group)
Demonstration
Conclusion

## Slide 3: Organizational Overview

## Slide 4: Mission and Vision of Digi Jadoo Broadband Limited(Mohammadi Group)
Mission:
1. Deliver Reliable & Affordable Broadband Connectivity
2. Enable Digital Transformation for Business & Household
3. Maintain Network Excellence & Customer Satisfaction
Vision:
1. Become Bangladesh’s Leading Broadband Service Provider
2. Bridge the Digital Divide
3. Foster Innovation in IoT , Smart Cities & Connected Infrastructure
4.Contribute to National Digital Economy Growth

## Slide 5: Office Information
Address of the Organization:
Name: Digi Jadoo Broadband Linited(Mohammadi Group)
Head-Office: Lotus Kamal Tower-One,Level-9,10,11,14,57 Joar Sahara C/A,Nikunja-2,Khilkhet,Dhaka-1229,Bangladesh.
Phone: +880 9613016503
Website: www.jadoobroadband.com
Email: noc@digijadoo.com
Figure 1: Organization picture

## Slide 6: Introduction

## Slide 7: Computer Network
Enables communication and resource sharing between devices
Consists of hardware (routers, switches, cables) and software (protocols, services)
Uses protocols like TCP/IP to ensure reliable communication
Enhances security through firewalls, encryption, and access control
Requires regular monitoring, maintenance, and troubleshooting

## Slide 8: Network Types
Figure 3: Local Area Network
Figure 4: Metroplitan Area Network

## Slide 9: Network Types(Contd.)
Figure 5: Wide Area Network

## Slide 10: Network Topology
Bus Network
Star Network
Ring Network
Tree Network
Mesh Network
Figure 6: Network Topology

## Slide 11: Network Model
OSI Model
OSI Model standardizes how network system communicates
Divided into 7 layers
Communication flows from top (Layer 7) to bottom (Layer 1) for sending data and bottom to top for receiving
Figure 7: Open System Interconnection

## Slide 12: IP Addressing
An IP address uniquely identifies a device on a network
IP addresses are essential for routing and communication between devices
Two versions exist: IPv4 (e.g., 192.168.1.1) and IPv6 (e.g., 2001:0db8::1)
IP addresses are divided into network and host portions
Can be static (manually assigned) or dynamic (assigned via DHCP)
Figure 8: An Example of IP Address

## Slide 13: Existing Network of Digi jadoo Broadband Limited

## Slide 14: Existing Network Model
Figure 9: Layout of Existing Network

## Slide 15: Network Devices
Core Router
Core Multilayer Switch
Distribution Switches(6)
PC’s(15)
Home-Router(2)
Servers(3)

## Slide 16: Routing Protocols
Static Routing
Dynamic Routing(OSPF, RIP)
Figure 10: Open Shorted Path Found
Figure 11: Dynamic Host Configuration Protocol

## Slide 17: Servers
MAIL Server
NTP Server
DHCP-DNS server

## Slide 18: Limitations of Existing Network
Network Congestion & Security risks
Limited IoT scalability
Vulnerable to Unauthorized access
Manual Management Only

## Slide 19: Proposed Network for Digi jadoo Broadband Limited(Mohammadi Group)

## Slide 20: Features of Proposed Network
Hierarchical design with core, distribution, and access layers for better IoT integration
IoT automation Control Via Home-Gateway and IoT Server
Improved manageability through layered design and logical VLAN segmentation(6 Zones)
Uses Giga Ethernet Cable for better data communication between Device
6 server (DHCP-DNS,Web,NTP,IoT,Syslog) for automated network Services

## Slide 21: Proposed Network Model
Figure 12: Layout of Proposed Network

## Slide 22: Proposed Network Model
Figure 12: Layout of Proposed Network

## Slide 23: Proposed Network Model
Figure 12: Layout of Proposed Network

## Slide 24: Network Devices
Core Router
Back up Router
Core Multilayer Switch
Distribution Switch(5)
Home-Router(2)
End Device(12)
Home-Gateway(4)
Servers(5)
IoT End Device(50)

## Slide 25: Servers
DHCP-DNS Server
WEB Server
NTP server
IoT Server
Syslog Server

## Slide 26: Demonstration

## Slide 27: Existing Network
Figure 13: Existing Network Demonstrates

## Slide 28: Proposed Network
Figure 14: Proposed Network Demonstrates

## Slide 29: Cost Estimation
Item | Quantity | Unit Price (USD) | Total (USD)
Cisco Layer 3 Core Switch | 1 | 4500 | 3500
Cisco Core Router and Backup router | 2 | 3500 | 7000
Distribution Switch | 5 | 1100 | 5500
Home-Gateway | 4 | 800 | 3200
Servers (DHCP-DNS, NTP, web,IoT,Syslog) | 5 | 4000 | 20000
Home Router | 2 | 400 | 800
IoT End Device | 50 | 500 | 25000
Total |  |  | 65,000

## Slide 30: Comparison between Existing and Proposed Network
Existing Network | Proposed Network
Weak/No Security Mechanism | Hierarchical topology (core, distribution, access layers)
Weak or absent security mechanisms | Enhanced security using Access Control Lists (ACLs)
No redundancy – prone to single points of failure | Redundant links and backup router ensure high availability.
Poor scalability and adaptability | Scalable VLAN and modular design supports future expansion
Not IoT Control | IoT Automation and Public wifi Service

## Slide 31: Conclusion

## Slide 32: Conclusion
This project successfully delivered a Next-Generation Smart City Infrastructure that transforms flat, unmanaged networks into secure, scalable, IoT-enabled environments.
Key Achievements:
Hierarchical 3-tier design (Core MLS, Distribution HG, 5 Access switches) replacing single broadcast domain
6-VLAN segmentation (Residential/Commercial/Govt/WiFi/IoT/Servers) providing zone isolation & security
Automated IoT control: 14 street lights + 4 traffic signals via centralized Home Gateway dashboard
Enterprise services: DHCP/DNS/NTP/Web/IoT/Syslog for centralized management & monitoring
Multi-layer security: ACL, Port Security, DHCP Snooping, SSH encryption across all zones

## Slide 33: Reference
[1] Academy, C. N. (2022). Packet Tracer User Guide. Retrieved from https://www.computernetworkingnotes.com
[2] geeksforgeeks. (2021). Wired and Wireless Networking. Retrieved from https://www.geeksforgeeks.org
[3] geeksforgeeks. (2025). Network Devices (Hub, Repeater, Bridge, Switch, Router, Gateways and Brouter). Retrieved from geeksforgeeks https://www.geeksforgeeks.org
[4] networklessons. (n.d.). ASA Firewall. Retrieved from https://networklessons.com
[5] What Is a Subnet Mask? Definition, Working, and Benefits. (2022). Retrieved from SpiceWorks https://www.spiceworks.com
[6] Yasar, K. (2023). IP address (Internet Protocol address). Retrieved from https://www.techtarget.com
https://www.techtarget.com